## Slide 1: Arithmetic for Computers

## Slide 2: What we have learned …
Integer number representation
  Decimal
  Binary Representation
  Hexadecimal

## Slide 3: Arithmetic for Computers
Operations on integers
  Addition and subtraction
  Multiplication and division
  Dealing with overflow
Floating-point real numbers
  Representation and operations
§3.1 Introduction

## Slide 4: Integer Addition
Example: 7 + 6
§3.2 Addition and Subtraction
Overflow if result out of range
  Adding +ve and –ve operands, no overflow
  Adding two +ve operands
    Overflow if result sign is 1
  Adding two –ve operands
    Overflow if result sign is 0

## Slide 5: Integer Subtraction
Add negation of second operand
Example: 7 – 6 = 7 + (–6)
  +7: 0000 0000 … 0000 0111 –6: 1111 1111 … 1111 1010 +1: 0000 0000 … 0000 0001
Overflow if result out of range
  Subtracting two +ve or two –ve operands, no overflow
  Subtracting +ve from –ve operand
    Overflow if result sign is 0
  Subtracting –ve from +ve operand
    Overflow if result sign is 1

## Slide 6: Dealing with Overflow
Some languages (e.g., C) ignore overflow
  Use MIPS addu, addui, subu instructions
Other languages (e.g., Ada, Fortran) require raising an exception
  Use MIPS add, addi, sub instructions

## Slide 7: Logic Design
Electronics in modern computers is digital, distinguishing only high and low voltage.
A signal that is true, or 1, is asserted, a signal that is false, or 0 is deasserted.
0 and 1 are called complement or inverse of one another
Logic blocks are two types
  Combinational – block without memory
  State – output depends on but input and memory

## Slide 8: Example: Logic Block

## Slide 9: Specify Logic Blocks - 1

## Slide 10: Specify Logic Blocks - 1
Boolean Algebra
  The OR operator + , e.g, A + B (logical sum)
  The AND operator . , e.g., A . B (logical product)
  The unary operator NOT Ā

## Slide 11: Laws of Boolean Algebra

## Slide 12: Gates – imp. of basic logic functions
Logic blocks are build form gates
Gates – Are implementations of basic logic functions
AND gates – implementation of AND function
OR gates – implementation of OR functions
NOT gates – implementation of inverse
From left to right

## Slide 13: Other Basic Building Elements
Decoder

## Slide 14: Decoder
Notes: 3 inputs 2^3 = 8 output

## Slide 15: Other Basic Building Elements
Multiplexors
  A multiplexor might properly be called as selector
  Its output is one of the inputs that is selected by the control
Example: Two input multiplexor

## Slide 16: Don’t Care
We do not care some input/output because another output is true or other subset of the input combinations determines the output

## Slide 17: Construction of a Basic ALU
ALU – Arithmetic Logic Unit
It does
  Generates random numbers
  Addition, subtraction , logical operations AND, OR
Construction of ALU
  AND gates, OR gates, Inverter, Multiplexer

## Slide 18: 1-bit ALU
Logical unit for AND and OR

## Slide 19: 1-bit ALU
Addition
  Two input for operands
  One output for the sum
  One output for CarryOut
  Another input for CarryIn

## Slide 20: Truth Table Specification
1-bit adder

## Slide 21: Logical Equation
CarryOut

## Slide 22: Equation Sum

## Slide 23: 1-bit ALU (AND, OR, Adder)

## Slide 24: 32-bit ALU (Adder)

## Slide 25: Content Covered
Chapter 3
  Section 3.1,3.2
Appendix B
B.1,B.2,B.3 (decoder, multiplexer)
B.5