## Slide 1: Arithmetic for Computers
Continue……

## Slide 2: Announcement
Midterm Friday
Time : 6:30 to 8:30
Location : ABB 102
Already posted in avenue

## Slide 3: Example: Logic Block

## Slide 4: Specify Logic Blocks - 1

## Slide 5: Specify Logic Blocks - 2
Boolean Algebra
  The OR operator + , e.g, A + B (logical sum)
  The AND operator . , e.g., A . B (logical product)
  The unary operator NOT Ā

## Slide 6: Gates – imp. of basic logic functions
Logic blocks are build form gates
Gates – Are implementations of basic logic functions
AND gates – implementation of AND function
OR gates – implementation of OR functions
NOT gates – implementation of inverse
From left to right

## Slide 7: Other Basic Building Elements
Decoder

## Slide 8: Decoder
Notes: 3 inputs 2^3 = 8 output

## Slide 9: Other Basic Building Elements
Multiplexors
  A multiplexor might properly be called as selector
  Take several data values and a selector or control
  Its output is one of the inputs that is selected by the control
  C = (A  S) + (B  S̅)
Example: Two input multiplexor

## Slide 10: 1-bit ALU (AND, OR, Adder)

## Slide 11: 32-bit ALU (Adder)

## Slide 12: Constructing an ALU
The arithmetic logic unit (ALU) is the brawn of the computer
The operation is controlled through the ALU Control Lines
  000 AND
  001 OR
  010 Add
  110 Subtract
  111 Set-on-less-than

## Slide 13: ALU - Subtraction
Subtraction is same as adding – (negative) operand
Recall how to get a negative number?
  2’s complement
    Flip bits (0 -> 1 and 1 -> 0)
    Add 1
How can we calculate A –B IN ALU with minor changes?

## Slide 14: 1-bit ALU (AND, OR, Adder)

## Slide 15: ALU – Subtraction with minor changes. How?
Consider adding the following features:
  Option of use bitwise NOT A
  Option to use bitwise NOT B
  Option to use bitwise A XOR B
  Option to set 0 as of the first CarryIn
  Option to set 1 as of the first CarryIn
What is needed?
  1 alone
  Both 1 and 2
  Both 3 and 4
  Both 2 and 5
  None of the above

## Slide 16: Step – 1
Adding 2:1 multiplexor
  Flips the bits

## Slide 17: Step - 2
Adding one after complement
a – b = a + complement of (b) + 1

## Slide 18: ALU – add, sub, or, and

## Slide 19: ALU – set-on-less-than
slt $t0, $t1, $t2
  Means
  If ($t1 < $t2 )
  $t0 = 1
  Else $t0 = 0

## Slide 20: ALU – set-on-less-than
After the comparison in result register
  Least significant would be 0/1
  Rest of the bits are 0
a – b < 0
  => a – b + b < b
    => a < b
If a is less than b, a – b is negative
  Negative representation has 1 in most significant bit (1)
  slt needs
If a is not less than b, a – b is positive
  Positive representation has 0 in most significant bit (0)
  slt need 0

## Slide 22: Complete ALU

## Slide 23: Practice
How to implement beq

## Slide 24: What signals accomplish ADD?
Binvert CarryIn Operator
1 0 2
0 1 2
1 1 2
0 0 2
None of the above

## Slide 25: What signals accomplish OR?
Binvert CarryIn Operator
1 0 0
0 1 1
1 1 1
1 0 1
None of the above

## Slide 26: What signals accomplish SUB?
Binvert CarryIn Operator
1 0 2
0 1 2
1 1 2
1 0 2
None of the above

## Slide 27: What signals accomplish STL?
Binvert CarryIn Operator
1 0 2
0 1 2
1 1 3
0 0 3
None of the above

## Slide 28: What we have covered?
Appendix B.5