## Slide 1: Faster Addition

## Slide 2: Faster addition
Determining the carry n sooner => speeding up
Fewer gates in sequence but many more gates
Worse case scenario is a function of log2n
Unlike software, hardware executes I parallel whenever inputs change

## Slide 3: Fast Carry Using infinite Hardware
carryIn for bit2 is CarryOut of bit 1

## Slide 4: Fast Carry: Propagation, Generation
Limit the complexity of the equation to simplify the hardware
C2 = (a1.b1) + (a1+b1).((a0.b0) + (a0+b0).c0)
ai.bi generate(gi) and (ai+bi) propagate(pi)

## Slide 5: Fast Carry: Propagation, Generation

## Slide 6: Fast Carry: Propagation, Generation

## Slide 7: Fast Carry: Second Level Abstraction
Perform carry look ahead for 4-bit adders
Super propagate

## Slide 8: Fast Carry: Second Level Abstraction
Perform carry look ahead for 4-bit adders
Super generate

## Slide 9: Fast Carry: Second Level Abstraction
Perform carry look ahead for 4-bit adders
Carry

## Slide 10: Performance
Carry look ahead vs Ripple Carry
Time: counting the number of gates along the path
Performance for two 16-bits adders
  Using tipple carry = 16*2 = 32
  Using two-level carry look ahead = 2 + 2 + 1

## Slide 11: What we have covered?
Appendix B.6