## Slide 1: Arithmetic for Computers
Continue……

## Slide 2: Complete ALU

## Slide 4: Multiplication
Length of the product is sum of lengths of operands

## Slide 5: Sequential Version
32
Initialized to 0
Initialize 0
64
64

## Slide 6: Multiplication Hardware
Initially 0

## Slide 7: Using 4 bit – 2 X 3

## Slide 8: Optimized Multiplier
Perform steps in parallel: add/shift
One cycle per partial-product addition

## Slide 9: Faster Multiplier
Uses multiple adders
  Cost/performance tradeoff
Can be pipelined
  Several multiplication performed in parallel

## Slide 10: MIPS Multiplication
Two 32-bit registers for product
  HI: most-significant 32 bits
  LO: least-significant 32-bits
Instructions
  mult rs, rt / multu rs, rt
    64-bit product in HI/LO
  mfhi rd / mflo rd
    Move from HI/LO to rd
    Can test HI value to see if product overflows 32 bits
  mul rd, rs, rt
    Least-significant 32 bits of product –> rd

## Slide 11: Division
Check for 0 divisor
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division
  Do the subtract, and if remainder goes < 0, add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
10
101
1010
-1000
10
n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor
§3.4 Division

## Slide 12: Division Hardware
Initially dividend
Initially divisor in left half

## Slide 13: Divide 7 by 2

## Slide 14: Optimized Divider
One cycle per partial-remainder subtraction
Looks a lot like a multiplier!
  Same hardware can be used for both

## Slide 15: Faster Division
Can’t use parallel hardware as in multiplier
  Subtraction is conditional on sign of remainder
Faster dividers (e.g. SRT devision) generate multiple quotient bits per step
  Still require multiple steps

## Slide 16: MIPS Division
Use HI/LO registers for result
  HI: 32-bit remainder
  LO: 32-bit quotient
Instructions
  div rs, rt / divu rs, rt
  No overflow or divide-by-0 checking
    Software must perform checks if required
  Use mfhi, mflo to access result

## Slide 17: What we have covered?
Sections 3.3 and 3.4