## Slide 1: Arithmetic for Computers
Continue……

## Slide 2: Floating Point
+125, -125 (Signed)
125 (unsigned)
3.14159265….ten (real numbers)
Non-integral numbers
  Including very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float (single precision) and double (double precision) in C
normalized
not normalized

## Slide 3: Floating Point Representation
–2.34 × 1056
  2.34  Significand
  56  Exponent (Actual)
  .34  Fraction / Mantissa
In binary
  ±1.xxxxxxx2 × 2yyyy
Representation of floating point follows Standard
§3.5 Floating Point

## Slide 4: Floating Point Standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)

## Slide 5: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always a leading 1 bit, so no need to represent explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single precision: Bias = 127
  Double precision: Bias = 1203
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits

## Slide 6: Floating-Point Example
Represent –0.75
  –0.75 = (–1)1 × 1.12 × 2–1
  S = 1
  Fraction = 1000…002
  Exponent = –1 + Bias
    Single: –1 + 127 = 126 = 011111102
    Double: –1 + 1023 = 1022 = 011111111102
Single: 1011111101000…00
Double: 1011111111101000…00

## Slide 7: Convert Floating-point Number
What is 1100 0001 0010 0000 0000 0000 0000 0000 ?
  - 1.010 X 2130
  - 10
  + 10
  + 1.010 X 2130
  None of the above
S
Exponent
Fraction
single: 8 bits
single: 23 bits

## Slide 8: Floating-Point Example
What number is represented by the single-precision float
11000000101000…00
  S = 1
  Fraction = 01000…002
  Fxponent = 100000012 = 129
x = (–1)1 × (1 + 012) × 2(129 – 127)
  = (–1) × 1.25 × 22
  = –5.0

## Slide 9: Floating Point Numbers

## Slide 10: Floating-point Additionten
Consider a 4-digit decimal example
9.999 X 101 + 1.610 X 10-1
Align decimal point: shift number with smaller exponent
  9.999 X 101 + 0.016 X 101
Add significands
  9.999 X 101 + 0.016 X 101 = 10.015 X 101
Normalize result & check for over/underflow
  1.0015 X 102
Round and normalize if necessary
  1.002 X 102

## Slide 11: Floating-point Additiontwo
Now consider a 4-digit binary example
1.000two X 2-1 + -1.110two X 2-2 = 0.5ten + -0.4375ten
Align binary points: shift number with smaller exponent
1.000two X 2-1 + -0.1110two X 2-1
Add Significands
0.001two X 2-1
Normalize result & check for over/underflow
  1.000two X 2-4, no over/underflow
Round and renormalize if necessary
  1.000two X 2-4 (no change) = 0.0625

## Slide 12: What we have covered?
Sections 3.5 (partial)