## Slide 1: Arithmetic for Computers
Continue……

## Slide 2: Floating Point
+125, -125 (Signed)
125 (unsigned)
3.14159265….ten (real numbers)
Non-integral numbers
  Including very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float (single precision) and double (double precision) in C
normalized
not normalized

## Slide 3: Floating Point Representation
–2.34 × 1056
  2.34  Significand
  56  Exponent (Actual)
  .34  Fraction / Mantissa
In binary
  ±1.xxxxxxx2 × 2yyyy
Representation of floating point follows Standard
§3.5 Floating Point

## Slide 4: Floating Point Standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)

## Slide 5: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always a leading 1 bit, so no need to represent explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single precision: Bias = 127
  Double precision: Bias = 1203
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits

## Slide 6: Floating-Point Example
Represent –0.75
  –0.75 = (–1)1 × 1.12 × 2–1
  S = 1
  Fraction = 1000…002
  Exponent = –1 + Bias
    Single: –1 + 127 = 126 = 011111102
    Double: –1 + 1023 = 1022 = 011111111102
Single: 1011111101000…00
Double: 1011111111101000…00

## Slide 7: Convert Floating-point Number
What is 1100 0001 0010 0000 0000 0000 0000 0000 ?
  - 1.010 X 2130
  - 10
  + 10
  + 1.010 X 2130
  None of the above
S
Exponent
Fraction
single: 8 bits
single: 23 bits

## Slide 8: Floating-Point Example
What number is represented by the single-precision float
11000000101000…00
  S = 1
  Fraction = 01000…002
  Fxponent = 100000012 = 129
x = (–1)1 × (1 + 012) × 2(129 – 127)
  = (–1) × 1.25 × 22
  = –5.0
(-1) X 1.012 X 22
= -101.00
= -5.0

## Slide 9: Floating Point Numbers
value | sign | exponent | fraction
0.0 | 0 or 1 | 0000 0000 | 0000 …. 0000
Sub/denormal | 0 or 1 | 0000 0000 | Anything but allzeros
+infinity | 0 | 1111 1111 | 0000 …. 0000
-infinity | 1 | 1111 1111 | 0000 …. 0000
NaN (Not a Number) | X | 1111 1111 | Anything but all zeros
Hidden bit is 0

## Slide 10: Floating-point Additionten
Consider a 4-digit decimal example
9.999 X 101 + 1.610 X 10-1
Align decimal point: shift number with smaller exponent
  9.999 X 101 + 0.016 X 101
Add significands
  9.999 X 101 + 0.016 X 101 = 10.015 X 101
Normalize result & check for over/underflow
  1.0015 X 102
Round and normalize if necessary
  1.002 X 102

## Slide 11: Floating-point Additiontwo
Now consider a 4-digit binary example
1.000two X 2-1 + -1.110two X 2-2 = 0.5ten + -0.4375ten
Align binary points: shift number with smaller exponent
1.000two X 2-1 + -0.1110two X 2-1
Add Significands
0.001two X 2-1
Normalize result & check for over/underflow
  1.000two X 2-4, no over/underflow
Round and renormalize if necessary
  1.000two X 2-4 (no change) = 0.0625

## Slide 12: Floating-point Multiplication
Multiply 0.5ten and -0.4375ten
  1.000two X 2-1 by -1.110two X 2-2
Adding the Actual exponent and find the exponent
  -1 + (-2) = -3 , -3 + 127 = 124
Multiply the significands
  1.000two X 1.110two = 1110000two -> 1.110000two X 2-3 -> 1.110 X 2-3
Normalize result & check for over/underflow
  Already normalized
  127 >= -3 >= -126 or 254 >= 124 >= 1 (so no over/underflow)

## Slide 13: Floating-point Multiplication
Round and renormalize if necessary
  1.110two X 2-3
Determine the Sign
  -1.110two X 2-3 (two operands has different sign)
Convert form binary to decimal
-1.110two X 2-3 = -0.001110two = -0.21875ten

## Slide 14: FP Instructions in MIPS
Single-precision arithmetic
  add.s, sub.s, mul.s, div.s
    e.g., add.s $f0, $f1, $f6
Double-precision arithmetic
  add.d, sub.d, mul.d, div.d
    e.g., mul.d $f4, $f4, $f6
Single- and double-precision comparison
  c.xx.s, c.xx.d (xx is eq, lt, le, …)
Branch on FP condition code true or false
  bc1t, bc1f
    e.g., bc1t TargetLabel

## Slide 15: FP Registers
Separate FP registers
  32 single-precision: $f0, $f1, … $f31
  Paired for double-precision: $f0/$f1, $f2/$f3, …
    Named by the even register

## Slide 16: Accurate Arithmetic
IEEE Std 754 specifies additional rounding control
  Extra bits of precision (guard, round, sticky)
Choice of rounding modes
  Truncate
  Round toward positive infinity
  Round toward negative infinity
  Round to nearest

## Slide 17: Accurate Arithmetic
Truncate
                g r s
  1.11000000000000000000100 0 0 0
  1.11000000000000000000100 (mantissa used)
  1.11000000000000000000110 1 1 0
  1.11000000000000000000110 (mantissa used)
  1.00000000000000000000111 0 1 1
  1.00000000000000000000111 (mantissa used)

## Slide 18: Accurate Arithmetic
Round toward positive infinity
  Positive numbers rounded one up if any of the g or r or s bit is one

## Slide 19: Accurate Arithmetic
Round toward negative infinity
    Negative numbers rounded one up if any of the g or r or s bit is one

## Slide 20: Accurate Arithmetic
Round to nearest
    Round down 0 – 3
    Round up 5-7
    If odd round up, if even no change - 4

## Slide 21: What we have covered?
Sections 3.5