## Slide 1: Memory Hierarchy

## Slide 2: Principal of locality
Temporal Locality
  If an item is referenced, it will tend to be referenced again
Spatial Locality
  If an item is referenced, items close by will tend to be referenced.

## Slide 3: Memory Hierarchy
Takes Advantages of Locality
  Everything on Disk
  Copy form disk to smaller DRAM : main memory
  Copy form DRAM to smaller SRAM : cache
Notes: Dynamic random access meory, Static random access memory,

## Slide 4: Memory Hierarchy
It is a structure
  Uses multiple levels of memories
  Distanced from processor
  As the distance from processor increase
    The size increases
    Speed reduced
    Cost reduced
    Access time increases

## Slide 5: Basic Structure of Memory Hierarchy

## Slide 6: Memory Hierarchy
Data is also hierarchical
  L1 < L2
At a time data is copied
  Between only two adjacency
  levels

## Slide 7: Some Terminologies
A Block or Line
  Minimum unit of information that can be presented or not presented
Hit
  Data Requested by the processor found in the upper level
Miss
  Data is not found it the upper level
  The lower level is accessed to get the data

## Slide 8: Some Terminologies…..
Hit rate or hit ratio
  Hit/access
  It is often used to measure the performance
Miss rate
  1 – hit rate
The time to service hit and miss is important
  Hit times
    Time to access the upper level
    Time needed to determine a hit or a miss

## Slide 9: Some Terminologies…..
Miss Penalty
  Time to replace a block in upper level with a corresponding block in the lover level
  Plus the time to deliver it to the processor

## Slide 10: The Basic of Caches
Cache:
  A safe place for hiding or storing things.
Simple Cache
  Processor requests are each one words
  Blocks also consists of a single word

## Slide 11: Simple Cache

## Slide 12: Two Questions?
How do we know if a data item is in the cache?
How do we find it?
By using the concept direct map

## Slide 13: Direct Map
Each word can go exactly at one place in the cache
Assign the cache location base on the address of the word in memory
This cache structure is called direct mapped cache

## Slide 14: Mapping?
Larger amount need to map with smaller amount
Lets do an example
  8 – block cache = 23
  Memory address 1ten (00001two) – 31ten (11111two)

## Slide 15: Direct Map (Index)

## Slide 16: Multiple data in single place!
How do we know data corresponds to a requested word?
By using a set of tags
Tags
  Contains the address information to identify a word
  Upper portion of the word address
  Upper 2 of the 5 bits address

## Slide 17: Valid bit
Valid bit checks where this index had any data or not

## Slide 18: Accessing a Cache

## Slide 19: Accessing a Cache

## Slide 20: Accessing a Cache

## Slide 21: Accessing a Cache

## Slide 22: Accessing a Cache

## Slide 23: Accessing a Cache

## Slide 24: Accessing a Cache

## Slide 25: Accessing a Cache

## Slide 26: Accessing a Cache

## Slide 27: Accessing a Cache

## Slide 28: Accessing a Cache

## Slide 29: Accessing a Cache