## Slide 1: Memory Hierarchy

## Slide 2: Accessing a Cache

## Slide 3: Accessing a Cache

## Slide 4: Spec of Memory Address
To uniquely identify a word address
  Index + tag code
Data existence
  Valid bit

## Slide 5: Bits Needed for a cache
Ia function of
  Cache size
  Address size

## Slide 6: Tag, total bits
Consider the scenario
  32 bit address
  A direct-map cache
  Cache size is 2n blocks, n bit for index
  The block size is 2m words, m bits are for words with in block
  2 bits are byte part
Tag = 32 – (m + n + 2)
Total bits = 2n * (block size + tag + valid field size)

## Slide 7: Reference address

## Slide 8: Tag, total bits
Tag = 32 – (m + n + 2)
Total bits = 2n * (block size + tag + valid field size)
The naming convention is to exclude tag and valid bit

## Slide 9: Humber of bits
How many total bits are required for a direct-mapped cache with 16 KiB of data and 4-word blocks, assuming a 32-bit address?
4 words = 22
16 KiB = 16 * 210
= (16 * 8 )/32 * 210
= 212 words
Each block has = 4 * 32 = 128 bits of data
Notes: 1024 word = 1024 * 32 bits = 1024 * 32/8 = 1024 * 4 KiB (killobytes)
16 * 1024 = 16 * 8 * 1024 = (16*8)/32 * 1024 = 22 * 210 = 212

## Slide 10: Humber of bits
How many total bits are required for a direct-mapped cache with 16 KiB of data and 4-word blocks, assuming a 32-bit address?
Tag = 32 - 10 - 2 – 2
Total bits = 210 * (22 * 32 + 18 + 1)
= 1024 * (4 * 32 + 19)
= 1024 * 147
= 147 Kibibits
= 18.4 KiB (8 bits = 1 Byte)
Notes: 1024 word = 1024 * 32 bits = 1024 * 32/8 = 1024 * 4 KiB (killobytes)
16 * 1024 = 16 * 8 * 1024 = (16*8)/32 * 1024 = 22 * 210 = 212

## Slide 11: Mapping Address to Multi Word Cache Block
Consider a cache with 64 blocks and a block size of 16 bytes. To what block number does byte address 1200 map?
Answer:
The block number =
(Block address) modulo (Number of blocks in the cache)

## Slide 12: Mapping Address to Multi Word Cache Block
Block address = byte address / block size
= 1200/16
= 75
Block number = 75 modulo 64 = 11
1200 to 1215 will go to block number 11

## Slide 13: Larger blocks exploit spatial locality

## Slide 14: Miss Rate VS Block Size.
Increase the block size decrease the miss rate
Miss rate may go up if block size becomes a significant factor of cache size
  Number of blocks will become small
  Would be bumped before use
  Miss penalty will increase

## Slide 15: Larger blocks exploit spatial locality

## Slide 16: Cache Misses
On cache hit
  CPU proceeds normally;
on cache miss
  Stall the CPU pipeline
  Fetch block from next level of hierarchy
  Instruction cache miss: restart instruction fetch
  Data cache miss: complete data access

## Slide 17: Handling Writes
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
Write through: also update memory
  But makes writes take longer, e.g. if base CPI = 1, 10% of instructions are stores, write to memory take 100 cycles: effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately, only stalls on write if write buffer is already full

## Slide 18: Handling Writes
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately, only stalls on write if write buffer is already full
Write back alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
  When a dirty block is replaced, write it back to memory

## Slide 19: Covered
Section 5.3