## Slide 1: Memory Technologies
Measuring and improving cache performance

## Slide 2: Performance…
CPU time can be devided into
  Clock cycles the CPU spends in execution
  Clock cycle the CPU spends waiting for memory
  CPU time = (CPU execution clock cycles + Memory-stall clock cycles)
  * Clock cycle time

## Slide 3: Memory-Stall, Read-Stall Cycles
Memory-stall clock cycles = (Read-stall cycles + Write-stall cycles)
Read-stall cycles = (Reads/Program) * Read miss rate * Read miss penalty

## Slide 4: Write-Stall Cycles
Write-stall cycles= (Writes/Program * Write miss rate * Write miss penalty) + Write buffer stalls

## Slide 5: Write-through Cache Org.
Read and Write penalty are the same
If we assume that the write-buffer stalls are negligible
Memory-stall clock cycles= ( Memory accesses / Program) * Miss rate * Miss penalty

## Slide 6: Read-Write Same
We can also factor this as
Memory-stall clock cycles = (Instructions/ Program) * (Misses/ Instruction) * Miss penalty

## Slide 7: Calculating Cache Performance
Assume the miss rate of an instruction cache is 2% and the miss rate of the data
cache is 4%. If a processor has a CPI of 2 without any memory stalls and the
miss penalty is 100 cycles for all misses, determine how much faster a processor
would run with a perfect cache that never missed. Assume the frequency of all
loads and stores is 36%.

## Slide 8: Continue…
Instruction miss cycles = I * 2% * 100 = 2.00 I
Data miss cycles = I * 36% * 4% * 100 = 1.44 I

## Slide 9: Continue…
The total number of memory-stall cycles is
= 2.00 I + 1.44 I = 3.44 I.
Accordingly, the total
CPI including memory stalls is = 2 + 3.44 = 5.44

## Slide 10: Performance calculation cont…

## Slide 11: A Faster Processor
CPI = 1 instead of 2
CPI with cache miss = 1 + 3.44 = 4.44
4.44 time faster
Time spend on memory
  63%(3.44/5.44) to 77%(3.44/4.4)

## Slide 12: Other Factors
Hit time
Increase in cache size

## Slide 13: AMAT
Average Memory Access Time
  Average time to access memory considering both hit and miss
AMAT = Time for a hit + Miss rate * Miss penalty

## Slide 14: AMAT Example
Find the AMAT for a processor with a 1 ns clock cycle time, a miss penalty of 20 clock cycles, a miss rate of 0.05 misses per instruction, and a cache access time (including hit detection) of 1 clock cycle. Assume that the read and write miss penalties are the same and ignore other write stalls.

## Slide 15: AMAT Continue…
AMAT = Time for a hit + Miss rate * Miss penalty
= 1 + 0.05 * 20
= 2 clock cycles
AMAT = 2 * 1 = 2ns
Section 5.15, Fallacies and Pitfalls for more examples

## Slide 16: Reducing the Cache Misses
So far we have used direct Mapped
  Has a fixed location for each block
Fully Associative

## Slide 17: Fully Associative
A cache structure in which a block can be placed in any location in the cache.
To find a given block in a fully associative cache, all the entries in the cache must be searched
Have a separate comparator
Useful for small block size

## Slide 18: Set Associative
Several sets
  Fixed mapping to a set
  But inside set fully associative

## Slide 19: Direct-mapping

## Slide 20: Set-Associative

## Slide 21: Fully Associative

## Slide 22: Everything in terms of Set-Associative
Direct Mapping – One-way set associative
Full Associative – m-way set associative

## Slide 23: One-way set associative

## Slide 24: Two-way set associative

## Slide 25: Four-way set associative

## Slide 26: Eight-way (Full) set associative

## Slide 27: Pros and Cons
Reduce miss rate
Increate hit time

## Slide 28: What Covered
Section 5.4