## Slide 1: Parallel Processors from Client to Cloud
Section 6..1 – 6.6

## Slide 2: What is the take away?
Getting good speed-up on a multiprocessor while keeping the problem size fixed is harder than
getting good speed-up by increasing the size of the problem.

## Slide 3: Strong vs Weak Scalling
strong scaling:
Speedup achieved on a multiprocessor
without increasing the size of the problem.
weak scaling:
Speedup achieved on a multiprocessor while
increasing the size of the problem proportionally
to the increase in the number of processors.

## Slide 4: Memory Hierarchy
Total Memory = M
Number of Processor = P
Then the memory per processor for
  strong scaling is approximately M/P,
  For weak scaling, it is approximately M

## Slide 5: Take Away
?

## Slide 6: Memory Hierarchy
Memory hierarchy can interfere with the conventional wisdom about weak scaling being easier than strong scaling
In case have no space in last level cache would result a worse performance.

## Slide 7: Speed-up Challenge: Balancing Load
For last class example we have assumed that
  The load was perfectly balanced
  That is, each of the 40 processors
  had 2.5% of the work to do

## Slide 8: Speed-up Challenge: Balancing Load
Show the impact on speed-up
one processor’s load is higher than all the rest
  Parallel load is 400
  5% to a processor
  12.5% to a processor

## Slide 9: Speed-up Challenge: Balancing Load
Show the impact on speed-up
one processor’s load is higher than all the rest
  Parallel load is 400
  5% to a processor?
  No of addition 5% × 400 or 20
  Other processors (39) will distribute 380

## Slide 10: Speed-up Challenge: Balancing Load
  No of addition 5% × 400 or 20
  Other processors (39) will distribute 380
The speed-up drops from 20.5 to 410t/30t = 14.

## Slide 11: Speed-up Challenge: Balancing Load
Show the impact on speed-up
one processor’s load is higher than all the rest
  Parallel load is 400
  12.5% to a processor
  The speed-up drops even further to 410t/60t = 7

## Slide 12: Take Away?
?

## Slide 13: Importance of Balancing Load
For just a single processor with twice the load of the others cuts speed-up by a third, and
Five times the load on just one processor reduces speed-up by almost a factor of three.

## Slide 14: Parallel Hardware Categories
SISD:
Single Instruction stream,
Single Data stream.
A uniprocessor
MIMD:
Multiple Instruction streams,
Multiple Data streams.
A multiprocessor.

## Slide 15: Parallel Hardware Categories
SPMD:
Single Program,
Multiple Data streams.
The conventional MIMD programming model,
where a single program runs across all processors
SIMD:
Opposite of MISD
Single Instruction stream,
Multiple Data streams.
The same instruction is applied to many data streams

## Slide 16: Vector
A vector architecture:
An elegant interpretation of SIMD
uses pipelined execution units

## Slide 17: Hardware Multithreading
programmer’s perspective of MIMD
MIMD relies on multiple processes or threads to try to keep multiple processors busy,
Hardware multithreading allows:
Multiple threads to share the functional units of a single processor
In an overlapping fashion to try to utilize the hardware resources efficiently.

## Slide 18: Thread
A thread includes
the program counter,
The register state, and
The stack.
It is a lightweight process;
whereas threads commonly share a single address space,
processes don’t.
thread switch can be instantaneous

## Slide 19: Process
A process includes
One or more threads,
The address space, and
The operating system state.
Hence, a process switch usually invokes the
operating system, but
Not a thread switch.

## Slide 20: Multithreading Approaches
Two main approaches
Fine-grained multithreading:
A version of hardware multithreading that implies switching between threads after every instruction.
Done in round-robin fashion, skipping any threads that are stalled
It can hide the throughput losses for stalls
It slows down the execution of the individual threads

## Slide 21: Multithreading Approaches
Two main approaches
Coarse-grained multithreading:
Switching between threads only after significant events (costly stall),
such as
a last-level cache miss.

## Slide 22: Hardware Multithreading
Simultaneous multithreading (SMT):
A version of multithreading
  that lowers the cost of multithreading by utilizing the resources needed for multiple issue,
  dynamically scheduled microarchitecture.

## Slide 23: What Covered
Section 6.2,6.3(partial),6.4(partial)